## Slide 1: Lab 1
LED & KEYPAD

## Slide 2: 建立一個類似 Sample Code 的新專案

## Slide 3: 新增資料夾
新增一個資料夾 Lab1，裡面再新增一個資料夾Keil。

## Slide 4
開啟 uVision5 > Project > New uVision Project
選擇剛建立的資料夾 Keil, 並給予新專案名稱 proj.

## Slide 5: 選擇Device
NuMicro Cortex-M Database
選擇NUC140VE3CN

## Slide 6: 新增Group
右鍵Target 1 → Manage Project Item…

## Slide 7: 新增Group
修改 Target 1 名稱
新增三個Group
  CMSIS
  Library
  User

## Slide 8: 新增檔案至CMSIS
system_NUC100Series.c
Library\Device\Nuvoton\NUC100Series\Source
startup_NUC100Series.s
Library\Device\Nuvoton\NUC100Series\Source\ARM

## Slide 9: 新增檔案至Library
clk.c
Library\StdDriver\src

## Slide 10: 新增檔案至User
SYS_init.c
Library\Nu-LB-NUC140\Source

## Slide 11: 新增main.c至User
Location 選擇到proj資料夾

## Slide 12: main.c
#include <stdio.h>
#include "NUC100Series.h"
#include "MCU_init.h"
#include "SYS_init.h"
int main(void)
{
SYS_Init();
}

## Slide 13: MCU_init.h
//Define Clock source
#define MCU_CLOCK_SOURCE
#define MCU_CLOCK_SOURCE_HXT // HXT, LXT, HIRC, LIRC
#define MCU_CLOCK_FREQUENCY 50000000 //Hz
//Define MCU Interfaces

## Slide 14: Project Configuration
Please refer to“3_SDK_Keil_MDK.ppt”for more details.
The following are some specific settings that you might want to know.

## Slide 15: Configure ->User
Run#1
  fromelf --bin ".\obj\@L.axf" --output ".\obj\@L.bin "
Run#2
  fromelf --text -c ".\obj\@L.axf" --output ".\obj\@L.txt"

## Slide 16: Configure ->C/C++ ->Include Paths

## Slide 17: Configure ->Linker
--map --first='startup_NUC100Series.o(RESET)' --datacompressor=off --info=inline --entry Reset_Handler

## Slide 18: 連接開發板

## Slide 19: 實驗
Hint: Yon can make use of projects “GPIO_LED” and “GPIO_Keypad” for this lab.

## Slide 20: Lab1.1
用LED搭配按鍵分別顯示每個學號的二進位
Ex:D0987654
按鍵1顯示第一個學號數字 0, (以LED全亮代替)
按鍵2顯示第二個學號數字 9 = 1001(2)
按鍵3顯示第三個學號數字 8 = 1000(2)
…
7
4
5
6
1
2
3
( 備註: 按住按鍵, 執行上述動作. 放開按鍵, 停止動作. )

## Slide 21: Lab1.2
按鍵1左向右跑的旋轉跑馬燈
按鍵2=flash
按鍵3右向左跑的旋轉跑馬燈
( 備註: 按住按鍵, 執行上述動作. 放開按鍵, 停止動作. )